## Slide 1: Downloading Arduino
FOR MAC

## Slide 2: 1. Go to the website and download the software that corresponds with your device https://www.arduino.cc/en/Main/Software

## Slide 3: 2. Click ‘just download’

## Slide 4: The file is in Zip format; if you use Safari it will be automatically expanded. If you use a different browser you may need to extract it manually.

## Slide 5: 3. Copy the Arduino application into the Applications folder (or elsewhere on your computer).

## Slide 6: 4. Go to the following link and download x64 for Mac OSC 10.9 and above
http://www.ftdichip.com/Drivers/VCP.htm

## Slide 7: 5. Go to the following link and download the CH34X driver
https://drive.google.com/file/d/0BwVeB5VOPU4RY2xVdUU3Tmx5Rmc/view?pageId=108203614547461735102

## Slide 8: 6. Connect the board to your computer using the USB cable. The green power LED (labelled PWR) should go on.

## Slide 9: 7. Go back to the Arduino app and select your Arduino board. Go to tools > board > Arduino Genuino Uno

## Slide 10: 8. Select the port. Go to tools > port > /dev/cu.wchusbserial1410

## Slide 11: 7. Once the board and port options are correct, install a new library. Go to sketch > include library > manage libraries

## Slide 12: 8. Type in FastLED in the search bar and install the latest version (3.1.3)

## Slide 13: 9. Go back to manage libraries Go to sketch > include library > manage libraries