## Slide 1: Downloading Arduino
FOR WINDOWS

## Slide 2: 1. Go to the website and download the software that corresponds with your device https://www.arduino.cc/en/Main/Software

## Slide 3: 2. Click ‘just download’

## Slide 4: Choose ‘Save as’ to save the installation file on your Desktop. Or it may just download into your ‘Downloads’ folder.

## Slide 5: 3. If it downloaded to your ‘Downloads’ folder, open the folder and drag the file onto your desktop. Double click the arduino file icon on your desktop.

## Slide 6: If you get a Windows security warning, click “Run” to begin the installation.

## Slide 7: Click ‘I Agree’ for the licence agreement. Then click ‘Next’ for all the options to be installed

## Slide 8: Click “Install” and install all the device software, finally click “Close”

## Slide 9: Double click on the new desktop icon, and “Allow access” for the firewall warning

## Slide 10: 4. Connect the board to your computer using the USB cable. The green power LED (labelled PWR) should go on.

## Slide 11: Windows may try to search for device driver software – this is good if successful. If not successful, device driver will be downloaded later.

## Slide 12: 5. Setting up your Arduino Uno board: Click on “Tools” in the sketch window

## Slide 13: Select your Arduino board. Choose Arduino/Genuino Uno

## Slide 14: Again, in “Tools” select the port (e.g. ‘COM 4’) then go to Step 6. If “Port” is greyed out, you will now need to download the device driver software…..

## Slide 15: If the port is not there go to the link below, download the CH340 driver, follow the instructions
http://sparks.gogo.co.nz/ch340.html

## Slide 16: Now go back and choose the correct com port. You can check this in Device Manager.

## Slide 17: 6. Now try to upload the example sketch called ‘Blink’ to your Arduino board. File  Examples  01.Basics  Blink

## Slide 18: Now press the upload icon. If upload is successful, the small LED on the board will blink on and off.